## Slide 1: Kinetic analyses
Jacques Barbet

## Slide 2: Kinetic Modeling

## Slide 3: Kinetics
Many different applications:
  Chemical reactions
  Radioactive decay
  Ligand receptor binding kinetics
  Ligand internalization
  Pharmacokinetics
  …
Differential equations with time as the independent variable
  Simple equation
  Set (system) of equations

## Slide 4: Compartment modeling
Introduced in pharmacokinetics to replace the complexity of physiology by "ad-hoc" spaces (compartments) supposed homogenous at all times with respect to concentrations of chemical species of interest (water, proteins, drugs, tracers…)
Compartment modeling allows a more detailed approach of:
  quantities of substances in an organism,
  kinetics of synthesis, absorption, distribution, catabolism and elimination
Very complex models can be set-up that include in vivo interactions and distribution across different organs
Compartment modeling may be used in many different situations
Notations:
Fi = amounts of compound of interest in compartment i
V = compartment volume
kji = transfer rate constant from compartment i to j

## Slide 5: Two-compartment pharmacokinetic model
Two exponential blood curves: can be fitted using a two-compartment mammillary model
Two exponential fitting is easy, but extracting micro-constants is not
k2,1
k1,2
Compartment 1
F1
Central compartment
Vc
Compartment 2
F2
Dosing
kel
Assumed in fast equilibrium with blood
Sampling in compartment 1
Slow equilibrium with blood
Not Sampled
dF1(t)/dt = - (ke1+k21) F1(t) + k12 F2(t) F1(t) = M exp(- 1t) + N exp(- 2t)
dF2(t)/dt = + k21 F1(t) - k12 F2(t) F2(t) = O (exp(- 1t) - exp(- 2t))

## Slide 6: Radioactive decay
Modeling parent – daughter cascades
An analytical solution exists, but simulation of multiple generator elution is not easy
k1
Parent
F1
Daughter
F2
k2
dF1(t)/dt = - k1F1(t)
dF2(t)/dt = + k1 F1(t) - k2 F2(t)

## Slide 7: Chemical reaction
Reagents and products = compartments
Example: A + B  C, dC(t)/dt = ka A(t) B(t) – kd C(t)
Non-linear system:
An analytical solution exists, but how to do data fitting?
ka * F2
kd
Reagent 1
F1
Product
F3
ka * F1
kd
Reagent 2
F2
dF1(t)/dt = - ka F1(t) F2(t) + kd F3(t)
dF2(t)/dt = - ka F1(t) F2(t) + kd F3(t)
dF3(t)/dt = + ka F1(t) F2(t) - kd F3(t)

## Slide 8: Analytical solutions versus numerical simulations
In all 3 previous examples, there are analytical solutions to the systems of differential equations
In more complex situations, the system of differential equations becomes hardly tractable (complex inputs, higher order linear systems, non-linear equations)
Runge–Kutta methods are iterative methods for the approximation of solutions of ordinary differential equations developed around 1900 by C. Runge and M. W. Kutta
The Chu-Berman method is more recent (Chu SC, Berman M. An exponential method for the solution of systems of ordinary differential equations. Comm. ACM. 17: 699-702, 1974). It is very interesting when solutions are close to exponentials
In both cases, approximations of Fi(t+Δt) are obtained from Fi(t) and the derivatives of Fi(t) calculated from the system of differential equations
These iterative solutions are implemented in the software package, which also allows for parameter fitting using non-linear, weighted, least square methods

## Slide 9: Runge-Kutta methods
Problem: knowing x(t0), one can calculate dx(t0)/dt, but how to calculate x(t) for t > t0?
This correction method (aka Runge-Kutta method) gives a 4th order approximation, meaning that the error is in the range of h5. Reducing h minimizes the error for one step but increases the number of steps
Higher order Runge-Kutta and more sophisticated methods have been developed
The Chu-Berman method is similar. It assumes that the solution is locally close to an exponential. It requires a matrix representation of the system of differential equations
dx(t)/dt = f (t, x)
a = f (tn, xn) b = f (tn + h⁄2, xn + h⁄2 a) c = f (tn + h⁄2, xn + h⁄2 b) d = f (tn + h, xn + h c)
xn+1 = xn + h⁄6 (a + 2 b + 2 c + d)

## Slide 10: Software packages
Dose
kel
Vc
A SAAM31
C A one-compartment model
H PAR
C Dose is expressed as 100%
IC(1) 100
L(0,1) 2.000000E-01
H DAT
C Time (min) Observed Values (% of dose)
101F(1)
0 100
1.5 74.4
2 67.3
3 54.8
3.5 49.6
5 36.7
10 13.5
20 1.83
30 0.24
45 0.012
60 0.00061
C **************** END OF DECK
Very powerful, free of charge,
Not really easy or intuitive
Novotny JA, Greif P, Boston RC. WinSAAM: application and explanation of use. Adv Exp Med Biol. 2003;537:343-51

## Slide 11: Alternative: Kinetics
Less powerful than WinSAAM
Run as an add-in to Microsoft Excel
Reasonably fast
Try to be as intuitive as possible 
Everything in the same Excel worksheet
Easy transfer of data from your records
Use Excel graphics
Very flexible
Needs a PC

## Slide 12: How does it work?
Model, data, settings and results in a single Excel worksheet
A Visual Basic routine reads the worksheet and runs the simulation/parameter adjustment program
The Visual Basic routine calls functions contained in a dynamic linked library (DLL) written in Pascal (Delphi)
The functions of the DLL are relatively advanced:
  They compile all literal equations written in the Excel worksheet
  They solve the differential equation system using the Runge-Kutta or Chu-Berman algorithms
  They do non-linear weighted least-square adjustments of unknown parameters using the Levenberg-Marquardt algorithm
"Kinetics" works for all compartment models
For population kinetics use: "Population kinetics"

## Slide 13: Loading the add-in
Create a folder of your choice and copy the “Kinetics.xlam” file in it
Copy the “Kinex_32.dll” and “Kinex_64.dll” file in the C:\Windows folder (usually at the root of disk C:, needs administrator privileges)
Open Excel, go to Excel Options (location depends on Excel version), then to Complements and link the “Kinetics.xlam” file as a complement
A new “Expert addins” tab should show in the ribbon
By clicking on the tab, a “Kinetics” command should show
Note: works with Excel 32 bits and Excel 64 bits

## Slide 14: Excel data sheet

## Slide 15: PK modeling

## Slide 16: Aknowledgments
François Davodeau, Eric Frampas, Catherine Maurel, Patricia Le Saec, Nolwenn Fichou, Alain Faivre-Chauvet, Thibaud Mauxion, Manuel Bardiès (Centre de Recherche en Cancérologie de Nantes-Angers, Inserm U892, CNRS UMR 6299, Nantes)
Anne Gruaz-Guyon, Faysal Alshoukr (Centre de Recherche Biologique Bichat Beaujon, Inserm U773, Paris)
Alshoukr, F., Rosant, C., Maes, V., Abdelhak, J., Raguin, O., Burg, S., Sarda, L. Barbet, J., Tourwé, D., Pelaprat, D., Gruaz-Guyon, A. Novel neurotensin analogues for radioisotope targeting to neurotensin receptor-positive tumors. Bioconj Chem., 2009, 20, 1602-1610.
Alshoukr F, Prignon A, Brans L, Jallane A, Mendes S, Talbot JN, Tourwé D, Barbet J, Gruaz-Guyon A. Novel DOTA-Neurotensin Analogues for 111In Scintigraphy and 68Ga PET Imaging of Neurotensin Receptor-Positive Tumors. Bioconjug Chem. 2011, 22, 1374-1385.
Frampas, E., Saï-Maurel, C., Thédrez, P., Remaud-Le Saëc, P., Faivre-Chauvet, A., Barbet, J. The intraportal injection model for liver metastasis: advantages of associated bioluminescence to assess tumour growth and influence on tumour uptake of radiolabelled anti-CEA antibody. Nucl Med Commun, 2011, 32, 147-154.
Frampas E, Maurel C, Remaud-Le Saëc P, Mauxion T, Faivre-Chauvet A, Davodeau F, Goldenberg DM, Bardiès M, Barbet J. Pretargeted radioimmunotherapy of colorectal cancer metastases: Models and pharmacokinetics predict influence of the physical and radiochemical properties of the radionuclide. Eur J Nucl Med Mol Imaging, 2011, 38, 271-273.

## Slide 17: Need for extended PK analysis
To go beyond point by point comparison of PK or biodistribution data or mere illustration:
  PK modeling and calculation of global parameters, especially clearance
PK analysis is often limited to blood (serum, plasma) data: this comes from the fact that, in the clinic, data are generally available from blood sampling only
PK analysis may also be used to deal with biodistribution data or sequential imaging
PK is of major interest for the calculation of absorbed doses (dosimetry):
  The Area Under the activity-time Curve (AUC) gives the total number of disintegrations

## Slide 18: Physiological modeling
Covell DG, Barbet J, Holton OD, Black CD, Parker RJ, Weinstein JN. Pharmacokinetics of monoclonal immunoglobulin G1, F(ab')2, and Fab' in mice. Cancer Res. 1986; 46: 3969-78.
Jain RK. Delivery of molecular and cellular medicine to solid tumors. Advanced Drug Delivery Reviews 2001; 46: 149–168
Muscles
Tumor

## Slide 19: Multi-compartment modeling
Stabin MG, Kooij PP, Bakker WH, Inoue T, Endo K, Coveney J, de Jong R, Minegishi A. Radiation dosimetry for indium-111-pentetreotide. J Nucl Med. 1997; 38: 1919-22.

## Slide 20: Simplified models
k2,1
k1,2
Compartment 1
F1
Central compartment
Vc
Compartment 2 F2
Dosing
kel
ki,1
k1,i
Tissue i
Fi+2
a specific compartment
+
a fraction in fast exchange with blood
Koeppe RA, Holthoff VA, Frey KA, Kilbourn MR, Kuhl DE. Compartmental analysis of [11C]flumazenil kinetics for the estimation of ligand transport rate and receptor distribution using positron emission tomography. J Cereb Blood Flow Metab. 1991; 11: 735-44.
Lammertsma AA, Bench CJ, Hume SP, Osman S, Gunn K, Brooks DJ, Frackowiak RS. Comparison of methods for analysis of clinical [11C]raclopride studies. J Cereb Blood Flow Metab. 1996; 16: 42-52.

## Slide 21: Differential equations
k2,1
k1,2
Compartment 1
F1
Compartment 2
F2
kel
ki,1
k1,i
Tissue i
Fi+2
dF1/dt = - (k2,1 + kel) F1 + k1,2 F2
dF2/dt = k2,1 F1 - k1,2 F2
dFi+2/dt = ki,1 F1 - k1,i Fi+2

## Slide 22: Modeling a multi-tissue biodistribution study
k2,1
k1,2
Compartment 1
F1
Compartment 2
F2
kel
ki,1
k1,i
Tissue i
Fi+2
Blood: | F1/A19 | Tumor: | F3+A14*F1 | Control tumor: | F4+A15*F1 | Liver: | F5+A16*F1 | Spleen: | F6+A17*F1 | Kidney: | F7+A18*F1
The different components: F1, F2…F10
The fixed parameters: P1, P2…P30 (may change at time interrupts)
The adjustable parameters: A1, A2…A30
Time: T
Names, like "Blood" or "k12", are allowed

## Slide 23: Least-square fit and maximum likelihood
If the squares of the deviations are weighted by the variance of the observations (wi = 1/σ(Yi)2), then the least square fit corresponds to the maximum likelihood.
Approximation: σ(Yi)2 = 0.21 . Yi1.4

## Slide 24: Weighting
In our software packages, data are weighted by giving the exponent (Error type)
The linear constant in σ(Yi)2 = A . YiErrorType is calculated from experimental data by the programs
Error type may be calculated as in the previous example when replicates are available
Otherwise, it is assumed from earlier knowledge
If the random variability of data follows a normal distribution (the general case since measurement errors result from a multitude of independent causes: central limit theorem) the exponent should be 2
If activity counting is the major cause of measurement error (Poisson distribution), the exponent should be 1
In practice, with radiolabeled compounds, the log-log regression almost always gives an exponent between 1 and 2 (if not, data have probably been forged)

## Slide 25: Parameter estimation algorithm
The software calculates the derivatives of the calculated values (Jacobian matrix) by changing each adjustable parameter at a time by 1%. This is quite time consuming for large numbers of adjustable parameters (parameter estimation may take up to a few minutes)
Then the weighted sum of square of residuals is iteratively minimized using the Levenberg-Marquardt algorithm (see H.P. Gavin, people.duke.edu/~hpgavin/ce281/lm.pdf)
As it is, the minimization process must be supervised. Reasonable guess must be made for starting parameter values and the Marquardt damping factor (Damping)
The algorithm stops when the sum of the squares of the relative changes in parameters is lower than a preset limit (Tolerance) or the maximum number of iterations is reached
When the algorithm has converged, asymptotic standard parameter errors (SD) on the estimated parameters are computed.

## Slide 26: examples

## Slide 27: Pharmacokinetics of an antibody in mouse
Biodistribution of 124I-HuA33 mAb in BALB/c Nude Mice Bearing SW1222 and Control (LIM 2537) Colon Carcinoma Xenografts |  |  |  |  |  | 
Time (Hours) | 4 | 24 | 48 | 96 | 168 | 240
Blood | 26.60 ± 2.91 | 15.14 ± 3.70 | 9.25 ± 1.52 | 4.79 ± 1.21 | 1.50 ± 0.38 | 0.52 ± 0.20
SW1222 tumor | 12.45 ± 1.39 | 31.58 ± 2.91 | 38.92 ± 5.41 | 49.99 ± 7.03 | 37.24 ± 5.38 | 17.28 ± 4.41
LIM 2537 tumor | 6.27 ± 0.80 | 6.19 ± 2.93 | 4.72 ± 2.93 | 3.86 ± 0.28 | 1.07 ± 0.27 | 0.25 ± 0.04
Liver | 8.07 ± 2.68 | 4.07 ± 0.93 | 0.88 ± 1.12 | 1.64 ± 0.41 | 0.29 ± 0.36 | 0.19 ± 0.21
Spleen | 6.45 ± 0.68 | 4.01 ± 1.81 | 9.58 ± 7.28 | 1.00 ± 0.48 | 2.64 ± 2.92 | 0.24 ± 0.05
Kidney | 9.64 ± 2.23 | 5.21 ± 1.24 | 1.76 ± 1.33 | 1.88 ± 0.35 | 1.12 ± 0.62 | 0.26 ± 0.09
Skin | 3.26 ± 0.18 | 5.49 ± 0.87 | 1.24 ± 1.39 | 1.57 ± 0.67 | 0.19 ± 0.11 | 0.21 ± 0.04
Bone | 2.60 ± 0.26 | 1.88 ± 0.59 | 4.37 ± 3.12 | 3.15 ± 3.77 | 1.31 ± 1.34 | 0.14 ± 0.05
Lung | 11.66 ± 1.50 | 6.49 ± 1.78 | 2.73 ± 1.67 | 2.14 ± 0.79 | 1.70 ± 0.96 | 0.39 ± 0.16
Heart | 7.62 ± 0.73 | 4.01 ± 1.07 | 3.58 ± 2.21 | 2.96 ± 2.58 | 0.56 ± 0.32 | 0.27 ± 0.09
Stomach | 5.31 ± 1.46 | 5.03 ± 5.09 | 1.12 ± 0.71 | 1.48 ± 0.08 | 0.35 ± 0.08 | 1.06 ± 0.17
Small bowel | 3.26 ± 0.82 | 2.88 ± 0.24 | 1.40 ± 0.77 | 0.44 ± 0.10 | 0.24 ± 0.10 | 0.38 ± 0.09
Lee FT, Hall C, Rigopoulos A, Zweit J, Pathmaraj K, O'Keefe GJ, Smyth FE, Welt S, Old LJ, Scott AM. Immuno-PET of human colon xenograft- bearing BALB/c nude mice using 124I-CDR-grafted humanized A33 monoclonal antibody. J Nucl Med. 2001;42:764-9.

## Slide 28: Blood pharmacokinetics: how many exponentials?
Semi-log plot
Linear plot

## Slide 29: Modeling a multi-tissue biodistribution study
Data from: Lee FT, Hall C, Rigopoulos A, Zweit J, Pathmaraj K, O'Keefe GJ, Smyth FE, Welt S, Old LJ, Scott AM. Immuno-PET of human colon xenograft- bearing BALB/c nude mice using 124I-CDR-grafted humanized A33 monoclonal antibody. J Nucl Med. 2001;42:764-9.

## Slide 30: Another example
Data from: Davodeau et al., personnal communication

## Slide 31: Another example

## Slide 32: Micro-constants and pharmacokinetic parameters
Compartmental modeling affords estimations of model micro-constants: ki,j, kel, etc.
These constants are usually not very useful
From these constants, more useful pharmacokinetic parameters can be calculated: e.g. distribution volumes, clearance
The area under the concentration–time or activity-time curves (AUC) are very important: they are used to calculate clearances and mean residence times
Half-lives are more easily obtained from a non-compartmental analysis
Clearance = dose / AUC = Vcentral kel: the volume of blood cleared of drug/tracer per unit time

## Slide 33: AUC and dosimetry
k2,1
k1,2
Compartment 1
F1
Compartment 2
F2
kel
ki,1
k1,i
Tissue i
Exp(-P1 T)
Accumulation i
One way to calculate AUC and Ãh is to include accumulation compartments in the model with decay correction in the transfer rate: EX(-P1*T)

## Slide 34: Other software packages

## Slide 35: Blood pharmacokinetics of albumin
By fitting two exponentials (no compartmental modeling)
Vc = 2.7 L, Vt = 10.8 L
[Albumin*](t) = Ro(1/Vc - 1/Vt) exp(- ln(2) t / T1/2) + Ro/Vt exp (- ln(2) t / T1/2)
AUC = Ro [(1/Vc - 1/Vt) T1/2 + 1/Vt T1/2] / ln(2)
Cl = Dose/AUC = ln(2) / [(1/Vc - 1/Vt) T1/2 + 1/Vt T1/2] = 0.5 L/day
Margen S, Tarver H. Comparative studies on the turnover of serum albumin in normal human subjects. J Clin Invest. 1956, 35, 1161-1172.
Wrong !

## Slide 36: Fitting multiple exponentials
By fitting 2 exponentials through the data, the T½ are 8.9 hours and 8.1 days
A better fit is obtained using 3 exponentials, with T½ of 0.3 hours, 13.2 hours and 10.2 days
Exponentials fitted using Exponentielles.xlam
Data collected from the figure using
PirateProject.exe

## Slide 37: A simple software for PK analysis
Pharmacokinetics.xlam runs with Excel for Windows and Excel 2004 for Mac.

## Slide 38: "Population kinetics"
One step approach (population analysis)
Estimation of
individual parameters
m ?
sd ?
#1
#2
#n
?
Non-linear mixed effect models
There are many advantages in the population approach including:
  considerable reduction in the number of required data per individual
  direct test of the inter-individual consistence of the data
  integration of covariates: mixed effects, i.e. determinist and stochastic
  possibility of using a priori information (Bayesian)

## Slide 39: "Interactions"
Using the same concepts as "Equilex", "Interactions" was made more appropriate for titration and speciation studies, but work equally well for multiple equilibriums in solution
"Interactions" may also be used for precipitation and liquid-liquid extraction studies
As "Equilex", it only deals with systems at thermodynamic equilibrium
See: "Interactions.pptx"